## Slide 1: Lab #4: PE controller
- Make a controller for the PE from Lab #3

## Slide 2: FAQ: Print log to console output
Try using $display(“output string”, ...);
  Works like printf() function in C.
  It prints output to TCL console.

## Slide 3: Practice: PE controller implementation

## Slide 4: Custom HW Example: Matrix Multiplication IP
MY_IP
Processing Element (PE)
Float32 MUL+ACC
[32:0] REG[0:127] (BRAM inference)
ADDR
DIN
DOUT
CTRL
TRUE DP
BRAM
C
B
A
DOUT
ADDR
FSM
[32:0] REG[0:127] (BRAM inference)
BRAM
INTERFACE
Shift(16)
PS
AXI_SLAVE INTERFACE
OUT
OUT
DIN
COUNTER
2-cyc
RESET

## Slide 5: PE controller
Fetches 2 vectors from memory and calculate inner product.
  Each vector contains 16 floating-point numbers.
Calculation is invoked by a single command (setting ‘start’ bit to 1).
When done, ‘done’ bit and ‘result’ are set by the controller.
Similar to (but not same with) FSM Example #2 in Lecture 3 (Verilog III)
Vector 0
Mem 0 - 15
Vector 1
Mem 16 - 31
PE Controller
‘start’ bit
‘done’ bit
result
32
Memory I/O

## Slide 6: Overview of PE controller
PE from lab #3
(given)
start
clk
reset
done
Your logic
rddata[WORD_SIZE – 1 : 0]
wrdata[WORD_SIZE – 1 : 0]
rdaddr[ADDR_BW - 1 : 0]
Control signals
Data ports
Given parameters
  WORD_SIZE : 32
  ADDR_BW : 5

## Slide 7: PE controller FSM
How it work?
  Having 4 states
    idle, load, calc, done
  Idle: wait for ‘start’ signal. If it is on, it moves to ‘load’ stage.
  Load: Load inputs to PE and controller’s memory.
  Calc: calculate input vectors. If it is done, moves to ‘done’ stage.
  Done: assign result to ‘wrdata’ port and turn ‘done’ bit on.
    ‘Done’ state lasts for 5 cycles. Turn ‘done’ off and shift to ‘idle’ state after 5 cycles.

## Slide 8: PE controller states
Idle
Done = 0
Load
Done = 0
Start = 0
Start = 1
Done
Done = 1
Calc
Done = 0
Not loaded
Load completed
Calculation
completed
Calculating
5 cycles passed
Less than
5 cycles passed
* Reset signal (omitted) unconditionally shifts your PE controller into Idle state

## Slide 9: Idle state
Wait for ‘start’ signal.
  If it is on, shift to ‘load’ stage.
‘done’ bit must be turned off in this state.
Idle
Load
Start = 0
Start = 1

## Slide 10: Load state
Request data to test bench
  Set ‘rdaddr’ to the address of the data you request.
  Requested data will be fetched to ‘rddata’ at next rising edge of the clock.
Test bench
xxxx
PE
Controller
0x13
Cycle 0
rdaddr
Test bench
Data[0x13]
PE
Controller
Cycle +2
rddata
Test bench
PE
Controller
0x18
Cycle +1
rdaddr
Data[0x18]
rddata
0x16
rdaddr
rddata

## Slide 11: Load state
PE
Store data to PE’s memory and controller’s memory.
  Store vector 0 (at mem[0] to mem[15]) to PE’s memory.
  Store vector 1 (at mem[16] to mem[31]) to controller’s memory.
Move to calc state if all the vectors are stored.
Controller
Memory
PE Memory
PE(given)
Vector 0 (mem[0 …15])
Vector 1 (mem[16 … 31])

## Slide 12: Calc state
Calculate dot product of vectors (from controller and PE memory).
Wait until dvalid is set (CAUTION: Don’t use wait() func. in module)
If calculation is done, move to ‘done’ state.
Calculate with given PE module.
Vector 0 : {a0, a1, a2, …., a15}
Vector 1 : {b0, b1, b2, …., b15}
(Vector 0) · (Vector 1) = {a0 * b0 + a1 * b1 + a2 * b2 + … + a15 * b15}
 Takes 16 cycles with floating-point IP (Lab #2, Lab #3)

## Slide 13: Done state
Assign output to ‘wrdata’ port.
Turn ‘done’ bit on.
This state lasts for 5 cycles.
  Shift to ‘idle’ state after 5 cycles.
  Turn off ‘done’ bit and set ’wrdata’ to zero.
Test bench
Wrdata :
0
PE
Controller
Cycle 0
Done : 0
Test bench
Wrdata :
result
PE
Controller
Cycle 1 - 5
Done : 1
Test bench
Wrdata :
0
PE
Controller
Cycle 6
Done : 0

## Slide 14: Test with given inputs
Given test bench loads and tests your controller with specified inputs.
  Check pe_controller_tb.v for input file specifications.
  Change the paths to your input files and run.
  Test bench will automatically score your implementation

## Slide 15: Run test bench
“Run all” to run whole test
  Test bench will automatically score your implementation
    If your score is 100, you can go home NOW! (Check TCL console output)

## Slide 16: Run test bench
“Run all” to run whole test
  Test bench will automatically score your implementation
    If your score is 100, you can go home NOW! (Check TCL console output)

## Slide 17: Grading policy
Check lists
  Correct calculation result. (8 points)
  ‘done’ bit should turned on for 5 cycles (1 point per cycle(2~5 cycle only))
  After 5 cycles, ‘done’ bit should be set to zero. (8 points)
    This score will not be given if you set ‘done’ bit to zero earlier.
    Also, result should be set to zero too.
Submit only “pe_controller.v” on eTL.
  Due : 4/3 (Tue) PM 11:59
  Late submission will result in penalty

## Slide 18: Appendix: Test with more cases (optional)
Test file generator(written in C) is uploaded at eTL.
  You can generate random input vector. (32 floating-point numbers)
  You can also convert your own input to hexadecimal form.
  For more details, please refer to enclosed readme.txt.
Please use with caution.
  Some generated values may be differ from Xilinx IP result by precision loss.
  In that case, please re-generate numbers.
  TA has verified that given inputs work correctly with Xilinx IP.

## Slide 19: Appendix: Detailed description of TB
Reset
start = 0
reset = 0
start
start = 1
reset = 1
Donestart = 0
reset = 1
Proc
start = 0
reset = 1
Unconditional
shift
Done = 1
Done = 0
5 cycles passed
Less than
5 cycles passed
Less than
5 cycles passed
5 cycles passed
All test finished
Finish
Print your score
Start
Load input
To TB memory