## Slide 1: Chapter # 1: Introduction Contemporary Logic Design

## Slide 2: Chapter Overview
Process of Design
Digital Systems
Design Representations
Rapid Prototyping

## Slide 3: The Process Of Design
Design
Initial concept: what is the function performed by the object?
Constraints: How fast? How much area? How much cost?
Refine abstract functional blocks into more concrete realizations
Notes: Design has three important facets:
A creative process of coming up with a vision of the solution
An engineering process of evaluating tradeoffs and making decisions among many alternatives
An optimization process of choosing the best combination of components to realize the vision.

## Slide 4
Implementation
Assemble primitives into more complex building blocks
Composition via wiring
Choose among alternatives to improve the design
Debug
Faulty systems: design flaws, composition flaws, component flaws
Design to make debugging easier
Hypothesis formation and troubleshooting skills

## Slide 6: The Art Of Design: Refinement of Representations
1. Functional Specification/What the System Does
Ex: Traffic Light Controller
Lights point in the directions N, S, E, W
Illuminates the same lights N as S and E as W
Cycles thru the sequence GREEN-YELLOW-RED
N-S and E-W never GREEN or YELLOW at the same time
Stay GREEN for 45 seconds, yellow for 15, red for 60

## Slide 7
2. Performance Constraints/Requirements to be Met
speed: compute changes in under 100 ms
power: consume less than 20 watts
area: implementation in less than 20 square cm
cost: less than $20 in manufacturing costs

## Slide 8: The Art of Design: "To Design Is To Represent"
1. English language specification
easy to write, but not precise and subject to ambiguity
2. Functional description
more precise specification
flow charts, program fragments
3. Structural description
complex components decomposed into
compositions of less complex components
4. Physical description
the design in terms of most primitive
building blocks, e. g., logic gates or
transistors

## Slide 9: The Process of Design
Top Down Design:
Complex functions replaced by more primitive functions
Bottom Up Design:
Primitives composed to build more and more complex assemblies
Rules of Composition and Correctness by Construction:
  Electrical Rules: how many components can be cascaded?
  Timing Rules: how does the system change in conjunction with
periodic triggering events?
Implementation as Assembly

## Slide 10: The Process of Design
Structural
Representation
decomposition of high level functions into more primitive functions
Top Down Decomposition

## Slide 13: The Process of Design
Rooms
Floor
Building
Bottom Up Assembly
Primitives composed to build
more and more complex assemblies
e.g., a group of rooms form a floor
a group of floors form a bldg.
e.g., a group of transistors form a gate
a group of gates form an addition circuit
addition circuits plus storage circuits
form a processor datapath

## Slide 14: The Process of Design: Debugging the System
Implementation does not meet functional specification
Logic design is incorrect (wrong function implemented)
Misinterpretation or corner cases ignored
Individual modules function correctly but their compositions do not
Misunderstanding of interface and timing behavior
Wiring mistakes, Electrical mistakes
Design Flaws
Implementation Flaws
Component Flaws
Logically correct and correctly wired
Not all hardware components are guaranteed to work!
E.g., burnt out component
What Can Go Wrong

## Slide 15: The Process of Design
Debugging via Simulation Before Construction
Debugging Skills:
Improving the testability of the design
Formulating a testing plan and choosing test cases
Hypothesizing about the cause of the problem
Isolating portions of the implementation for testing
Effective use of laboratory instruments for troubleshooting

## Slide 16: Digital Hardware Systems
Digital Systems
Digital vs. Analog Waveforms
Analog:
values vary over a broad range
continuously
Digital:
only assumes discrete values
0
0

## Slide 17: Digital Hardware Systems
Analog systems: slight error in input yields large error in output
Digital systems: more accurate and reliable
Readily available as self-contained, easy to cascade building blocks
Computers use digital circuits internally
Interface circuits (i.e., sensors & actuators) often analog
This course is about logic design, not system design (processor
architecture), not circuit design (transistor level)
Advantages of Digital Systems

## Slide 18: Digital Hardware Systems
Two discrete values:
yes, on, 5 volts, current flowing, magnetized North, "1"
no, off, 0 volts, no current flowing, magnetized South, "0"
Advantage of binary systems:
rigorous mathematical foundation based on logic
the three preconditions must be true to imply the conclusion
both the door must
be open and the car
running before I can
back out
IF N-S is green
AND E-W is red
AND 45 seconds has expired since the last light change
THEN we can advance to the next light configuration
IF the garage door is open
AND the car is running
THEN the car can be backed out of the garage
Digital Binary Systems

## Slide 19: Digital Hardware Systems
Algebra: variables, values, operations
In Boolean algebra, the values are the symbols 0 and 1
If a logic statement is false, it has value 0
If a logic statement is true, it has value 1
Operations: AND, OR, NOT
Boolean Algebra and Logical Operators

## Slide 20: George Boole (1815 – 1864)
영국 수학자.
The Mathematical Analysis of Logic, 1847
  AND, OR & NOT can perform all logic functions
  No practical use
    Forgotten until 1930s
Source: www.computerhistory.org

## Slide 21: Claude Shannon (1916 – 2001)
Encountered G. Boole’s ideas in a college philosophy class in 1930s.
1937 MIT 석사학위논문:
  A Symbolic Analysis of Relay and Switching Circuits
  Applied Boolean Algebra to the design of logic circuits
Source: www.computerhistory.org

## Slide 22: Digital Hardware Systems
IF the garage door is open
AND the car is running
THEN the car can be backed out of the garage
door open?
car running?
back out car?
false/0
false/0
true/1
true/1
false/0
true/1
false/0
true/1
false/0
false/0
false/0
TRUE/1
Hardware Systems and Logical Operators

## Slide 23: Digital Hardware Systems
Physical electronic components are continuous, not discrete!
These are the building blocks of all digital components!
Transition from logic 1 to logic 0
does not take place instantaneously
in real digital systems
Intermediate values may be visible
for an instant
Boolean algebra useful for describing the steady state behavior of
digital systems
Be aware of the dynamic, time varying behavior too!
The Real World

## Slide 24: Digital Hardware Systems
Integrated circuit technology
choice of conducting, non-conducting, sometimes conducting
("semiconductor") materials
whether or not their interaction allows electrons to flow forms
the basis for electrically controlled switches
Digital Circuit Technologies
Main technologies
MOS: Metal-Oxide-Silicon
Bipolar
Transistor-Transistor Logic
Emitter Coupled Logic

## Slide 25: Digital Hardware Systems
Transistor
basic electrical switch
three terminals: gate, source, drain
voltage between gate and source exceeds threshold
switch is conducting or "closed"
electrons flow between source and drain
when voltage is removed,
the switch is "open" or non-conducting
connection between source and drain is broken
MOS Technology

## Slide 26: Transistor as a Switch

## Slide 27: Digital Hardware Systems
Circuit that implements logical negation (NOT)
1 at input yields 0 at output
0 at input yields 1 at output
Inverter behavior as a function of input voltage
input ramps from 0V to 5V
output holds at 5V for some range of small
input voltages
then changes rapidly, but not instantaneously!
remember distinction between
steady state and dynamic behavior

## Slide 28: Digital Hardware Systems
Combinational logic
  no feedback among inputs and outputs
  outputs are a pure function of the inputs
  e.g., full adder circuit:
(A, B, Carry In) mapped into (Sum, Carry Out)
Network implemented from
switching elements or logic
gates.
The presence of feedback
distinguishes between sequential
and combinational networks.
Combinational vs. Sequential Logic

## Slide 29: Digital Hardware Systems
Sequential logic
inputs and outputs overlap
outputs depend on inputs and the entire history of execution!
network typically has only a limited number of unique configurations
these are called states
e.g., traffic light controller sequences infinitely through four states
new component in sequential logic networks:
storage elements to remember the current state
output and new state is a function of the inputs and the old state
i.e., the feedback inputs are the state!
period reference signal, the clock, causes the storage elements to
accept new values and to change state
Synchronous systems
Asynchronous systems
no single indication of when to change state

## Slide 30: Digital Hardware Systems
Traffic Light Example
Next State Logic
Maps current state and alarm events into the next state
Current State
Storage elements replaced by next state
when the clock signal arrives
Output Logic
Current state mapped into control signals
to change the lights and to start the event
timers
IF controller in state N-S green, E-W red
AND the 45 second timer alarm is asserted
THEN the next state becomes N-S yellow,
E-W red when the clk signal is next asserted
Combinational vs Sequential Logic

## Slide 31: Representations of a Digital Design
Switches
A switch connects two points under control signal.
when the control signal is 0 (false), the switch is open
when it is 1 (true), the switch is closed
when control is 1 (true), switch is open
when control is 0 (false), switch is closed
Normally Closed
Normally Open

## Slide 32: Representations of a Digital Design
Truth Tables
tabulate all possible input combinations and their associated
output values
Example: half adder
adds two binary digits
to form Sum and Carry
NOTE: 1 plus 1 is 0 with a
carry of 1 in binary
Example: full adder
adds two binary digits and
Carry in to form Sum and
Carry Out

## Slide 33: Representations of a Digital Design
Boolean Algebra
NOT X is written as X
X AND Y is written as X & Y, or sometimes X Y
X OR Y is written as X + Y
values: 0, 1
variables: A, B, C, . . ., X, Y, Z
operations: NOT, AND, OR, . . .
A
0
0
1
1
B
0
1
0
1
Sum
0
1
1
0
Carry
0
0
0
1
Sum = A B + A B
Carry = A B
OR'd together product terms
for each truth table
row where the function is 1
if input variable is 0, it appears in
complemented form;
if 1, it appears uncomplemented
Deriving Boolean equations from truth tables:

## Slide 34: Representations of a Digital Design
Gates
most widely used primitive building block in digital system design
Netlist: tabulation of gate inputs & outputs
and the nets they are connected to
Net: electrically connected collection of wires
Standard
Logic Gate
Representation
Half Adder Schematic

## Slide 35: Representations of a Digital Design: Gates
Full Adder Schematic
Fan-in: number of inputs to a gate
Fan-out: number of gate inputs an output is connected to
Technology "Rules of Composition" place limits on fan-in/fan-out

## Slide 36: Representations of a Digital Design
Waveforms
dynamic behavior of a circuit
real circuits have non-zero delays
Timing Diagram of the Half Adder
sum
propagation
delay
circuit hazard: 1 plus 0 is 1, not 0!
sum
propagation
delay
Output changes are delayed from input changes
The propagation delay is sensitive to paths in the circuit
Outputs may temporarily change from the correct value to the
wrong value back again to the correct value: this is called
a glitch or hazard

## Slide 37: Representations of a Digital Design
Blocks
structural organization of the design
black boxes with input and output connections
corresponds to well defined functions
concentrates on how the components are composed by wiring
Full Adder realized in terms of
composition of half adder blocks
Block diagram representation
of the Full Adder

## Slide 38: Representations of a Digital Design
Waveform Verification
Does the composed full adder behave the same as the full gate
implementation?
Sum, Cout waveforms lag input changes in time
How many time units after input change is it safe to examine
the outputs?

## Slide 39: Representation of a Digital Design:
ABEL Hardware Description Language
MODULE half_adder;
a, b, sum, carry PIN 1, 2, 3, 4;
TRUTH_TABLE {[a, b] -> [sum, carry]}
[0, 0] -> [0, 0];
[0, 1] -> [1, 0];
[1, 0] -> [1, 0];
[1, 1] -> [0, 1];
END half_adder;
MODULE half_adder;
a, b, sum, carry PIN 1, 2, 3, 4;
EQUATIONS
SUM = (A & !B) # (!A & B);
CARRY = A & B;
END half_adder;
Truth Table
Specification
Equation
Specification
AND
OR
NOT
Behaviors

## Slide 40: Representations of a Digital Design
Behaviors
-- ***** inverter gate model *****
-- external ports
ENTITY inverter_gate;
PORT (a: IN BIT; z: OUT BIT);
END inverter_gate;
-- internal behavior
ARCHITECTURE behavioral OF inverter_gate IS
BEGIN
z <= NOT a AFTER 10 ns;
END behavioral;
-- ***** and gate model *****
-- external ports
ENTITY and_gate;
PORT (a, b: IN BIT; z: OUT BIT);
END and_gate;
-- internal behavior
ARCHITECTURE behavioral OF and_gate IS
BEGIN
z <= a AND b AFTER 10 ns;
END behavioral;
Black Box View
as seen by outside
world
Internal Behavior
Note delay statement
Hardware description languages
structure and function of the digital design
Example: Half Adder in VHDL

## Slide 41: Representation of a Digital Design: Behaviors
-- ***** or gate model *****
-- external ports
ENTITY or_gate;
PORT (a, b: IN BIT; z: OUT BIT);
END or_gate;
-- internal behavior
ARCHITECTURE behavioral OF or_gate IS
BEGIN
z <= a OR b AFTER 10 ns;
END behavioral;
-- ***** half adder model *****
-- external ports
ENTITY half_adder;
PORT (a_in, b_in: INPUT; sum, c_out: OUTPUT);
END half_adder;
-- internal structure
ARCHITECTURE structural of half_adder IS
-- component types to use
COMPONENT inverter_gate
PORT (a: IN BIT; z: OUT BIT); END COMPONENT;
COMPONENT and_gate
PORT (a, b: IN BIT; z: OUT BIT); END COMPONENT;
COMPONENT or_gate
PORT (a, b: IN BIT; z: OUT BIT); END COMPONENT;
-- internal signal wires
SIGNAL s1, s2, s3, s4: BIT;
AND, OR, NOT models
typically included in a
library
Particular components
to be used within the
model of the half adder

## Slide 42: Representation of a Digital Design: Behaviors
BEGIN
-- one line for each gate, describing its type and connections
i1: inverter_gate PORT MAP (a_in, s1);
i2: inverter_gate PORT MAP (b_in, s2);
a1: and_gate PORT MAP (b_in, s1, s3);
a2: and_gate PORT MAP (a_in, s2, s4);
o1: or_gate PORT MAP (s3, s4, sum);
END structural;
Textual description
of the netlist
This VHDL specification corresponds to the following labeled schematic

## Slide 43: Rapid Electronic System Prototyping
quick construction of digital systems to prove concept
rapid exploration of alternative design approaches
performance traded off for faster path to implementation
Goals:
Techniques:
computer-aided design tools
  simulation: find out how the design will behave
before constructing it
  synthesis: generate detailed descriptions, like schematics,
from high level descriptions, like Boolean equations
quick turnaround implementation technologies
programmable logic

## Slide 44: Rapid Electronic System Prototyping:
Computer-Aided Design
Synthesis tools
create a portion of the design from other portions
map more abstract representation to more physical representation
Behavioral
Synthesis
VHDL
Verilog
…
Boolean
Equations
Logic
Synthesis
Gate
Libraries
Schematics
map a representation into a more optimized form of that representation, e.g., espresso
ABEL

## Slide 45: Rapid Electronic System Prototyping
Simulation
program which dynamically executes an abstract design description
obtain verification of functional correctness and some timing
information before the design is physically constructed
easier to probe and debug a simulation than an implemented design
simulation cannot guarantee that a design will work
only as good as the test cases attempted
does not check electrical errors
abstracts away some of the realities of a real system
Logic Simulation
Timing Simulation
design described in terms of logic gates
values are 0, 1 (plus others to be introduced)
good for truth table verification
waveform inputs and outputs
model of gate delays
are the waveform shapes what was expected?
identification of performance bottlenecks

## Slide 46: Rapid Electronic System Implementation
Rapid Implementation Technologies
the function and interconnect of a component can be "personalized"
alternative to discrete logic gates and wires
reduces wiring complexity and parts count
facilitates more rapid design changes and enhancements
Programming with 1's and 0's
component function configured through truth table
interconnect among internal modules also configured in this way
selectively blown fuses
programmable switching matrix configured by 1's and 0's

## Slide 47: Rapid Electronic System Prototyping
Example: Read-Only Memories
hardware implementation of a two dimensional array
inputs form the index into the array
the binary word at the indexed memory location contains the
output values
contents are programmed once, read many times
Half Adder Realized as a ROM:
Full Adder Realized as a ROM:

## Slide 48: Chapter Review
the process of design:
functional decomposition and design by assembly
the kinds of systems we will be designing:
combinational and sequential logic
binary digital systems
implemented in MOS and bipolar technology
the many levels of design representation:
from switches to behavioral descriptions
the changing technological landscape:
rapid electronic system implementation
facilitated by computer-aided design tools
(in particular, synthesis and simulation tools)
and programmable logic devices

## Slide 49
Backup Slides

## Slide 50: Motivation
Dramatic Change in the Way Industry Does Hardware Design
Pervasive use of Computer-Aided Design Tools
Deemphasis on hand design methods
Emphasis on abstract design representations
Hardware design begins to look like software design
Emergence of Rapid Implementation Circuit Technology
Programmable rather than discrete logic
Importance of Sound Design Methodologies
Synchronous Designs
Rules of Composition

## Slide 51: The Elements of Modern Design
Rapid Prototyping
Technologies
Design
Representations
Circuit
Technologies
MOS
TTL
Behaviors
Blocks
Waveforms
Gates
Truth Tables
Boolean Algebra
Switches
Simulation
Synthesis
PAL, PLA, ROM, PLD
Computer-Aided
Design
Representations, Circuit Technologies, Rapid Prototyping

## Slide 52: Representations of a Digital Design: Switches
Examples:
routing inputs to outputs through a maze
Floating nodes:
what happens if the car is not running?
outputs are floating rather than forced to be false
Under all possible control signal settings
(1) all outputs must be connected to some input through a path
(2) no output is connected to more than one input through any path

## Slide 53: Representations of a Digital Design: Switches
Implementation of AND and OR Functions with Switches
AND function
Series connection to TRUE
OR function
Parallel connection to TRUE

## Slide 54: Representations of a Digital Design: Boolean Algebra
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
Cin
0
1
0
1
0
1
0
1
Sum
0
1
1
0
1
0
0
1
Cout
0
0
0
1
0
1
1
1
Another example:
Sum = A B Cin + A B Cin + A B Cin + A B Cin
Cout = A B Cin + A B Cin + A B Cin + A B Cin

## Slide 55: Representations of a Digital Design: Boolean Algebra
Reducing the complexity of Boolean equations
Laws of Boolean algebra can be applied to full adder's carry out
function to derive the following simplified expression:
Cout = A Cin + B Cin + A B
Verify equivalence with the original Carry Out truth table:
place a 1 in each truth table row where the product term is true
each product term in the above equation covers exactly two rows
in the truth table; several rows are "covered" by more than one term

## Slide 56: Representations of a Digital Design
Gates
most widely used primitive building block in digital system design
Netlist: tabulation of gate inputs & outputs
and the nets they are connected to
Net: electrically connected collection of wires
Standard
Logic Gate
Representation
Half Adder Schematic

## Slide 57: Representations of a Digital Design: Gates
Full Adder Schematic
Fan-in: number of inputs to a gate
Fan-out: number of gate inputs an output is connected to
Technology "Rules of Composition" place limits on fan-in/fan-out

## Slide 58: Representations of a Digital Design: Waveforms
Tracing the Delays: A=0,B=0 to A=0,B=1
(i) Initial conditions
(ii) B changes from 0 to 1
10 time units
of delay
(iii) Output of top AND gate
changes after 10 time units
(iv) Output of OR gate
changes after 10 time units

## Slide 59: Tracing Hazard
1
1
1
0
1
0
A
1
0
B
0
0
SUM
CARR
Y
0
1
1
1
1
1
1
0
A
1
0
B
0
0
SUM
CARR
Y
0
0
1
0
0
1
1
0
A
1
0
B
0
0
SUM
CARR
Y
1
0
After 10 time units
0
0
0
1
1
0
A
1
0
B
1
0
SUM
CARR
Y
1
0
After 20 time units

## Slide 60: Tracing Hazard
0
0
0
1
1
0
A
1
0
B
1
0
SUM
CARR
Y
1
0
After 20 time units
1
0
0
1
1
0
A
1
0
B
1
0
SUM
CARR
Y
1
0
After 20 time units