## Slide 1: Chapter 6: Sequential Logic Design

## Slide 2: Sequential logic
Sequential circuits
  simple circuits with feedback
  latches
  edge-triggered flip-flops
Timing methodologies
  cascading flip-flops for proper operation
  clock skew
Asynchronous inputs
  metastability and synchronization
Basic registers
  shift registers
  simple counters
Hardware description languages and sequential logic

## Slide 3: Sequential circuits
C1
C2
C3
comparator
value
equal
multiplexer
reset
open/closed
new
equal
mux control
clock
comb. logic
state
Circuits with feedback
  outputs = f(inputs, past inputs, past outputs)
  basis for building "memory" into logic circuits
  door combination lock is an example of a sequential circuit
    state is memory
    state is an "output" and an "input" to combinational logic
    combination storage elements are also memory

## Slide 4: Circuits with feedback
X1 X2 • • • Xn
switching network
Z1 Z2 • • • Zn
How to control feedback?
  what stops values from cycling around endlessly

## Slide 5: Simplest circuits with feedback
"remember"
"load"
"data"
"stored value"
"0"
"1"
"stored value"
Two inverters form a static memory cell
  will hold value as long as it has power applied
How to get a new value into the memory cell?
  selectively break feedback path
  load new value into cell

## Slide 6: Memory with cross-coupled gates
R
S
Q
Q'
R
S
Q
R'
S'
Q
Q
Q'
S'
R'
Cross-coupled NOR gates
  similar to inverter pair, with capability to force output to 0 (reset=1) or 1 (set=1)
Cross-coupled NAND gates
  similar to inverter pair, with capability to force output to 0 (reset=0) or 1 (set=0)

## Slide 7: Timing behavior
Reset
Hold
Set
Set
Reset
Race
R
S
Q
\Q
100
R
S
Q
Q'

## Slide 8: State behavior or R-S latch
S R Q 0 0 hold 0 1 0 1 0 1 1 1 unstable
Truth table of R-S latch behavior
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
Q Q' 1 1
R
S
Q
Q'

## Slide 9: Theoretical R-S latch behavior
State diagram
  states: possible values
  transitions: changes based on inputs
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
Q Q' 1 1
SR=00
SR=11
SR=00
SR=10
SR=01
SR=00
SR=10
SR=00
SR=01
SR=11
SR=11
SR=10
SR=01
SR=01
SR=10
SR=11
possible oscillation between states 00 and 11
R
S
Q
Q'

## Slide 10: Observed R-S latch behavior
Very difficult to observe R-S latch in the 1-1 state
  one of R or S usually changes first
Ambiguously returns to state 0-1 or 1-0
  a so-called "race condition"
  or non-deterministic transition
SR=00
SR=00
Q Q' 0 1
Q Q' 1 0
Q Q' 0 0
SR=10
SR=01
SR=00
SR=10
SR=00
SR=01
SR=11
SR=11
SR=01
SR=10
SR=11
R
S
Q
Q'

## Slide 11: R-S latch analysis
Q(t+)
R
S
Q(t)
S R Q(t) Q(t+) 0 0 0 0 0 0 1 1 0 1 0 0 0 1 1 0 1 0 0 1 1 0 1 1 1 1 0 X 1 1 1 X
hold
reset
set
not allowed
characteristic equation
Q(t+) = S + R’ Q(t)
Break feedback path
R
S
Q
Q'
0 0
1 0
X 1
X 1
Q(t)
R
S

## Slide 12: J-K F/F
How to eliminate the forbidden state?
Idea: use output feedback to
guarantee that R and S are
never both one
J, K both one yields toggle
Characteristic Equation:
Q+ = Q K + Q J

## Slide 13: J-K Latch: Race Condition
Set
Reset
Toggle
Race Condition
Toggle Correctness: Single State change per clocking event
Solution: Master/Slave Flipflop
T F/F:
Formed from J-K with both inputs wired together

## Slide 14: Primitive Flows
R-S Latches (Forbidden State Problem)
J-K Latches (Toggle Problem)
Master-Slave F/F (Ones Catching Problem)
D F/F & Edge-Triggered F/F

## Slide 15: Activity: R-S latch using NAND gates
R’
S’
Q
Q'
characteristic equation
Q(t+) = S + R’ Q(t)
R’
S’
Q(t)
0 0
1 0
X 1
X 1
Q(t)
R
S
S R S’ R’ Q(t) Q(t+) 0 0 1 1 0 0 0 0 1 1 1 1 0 1 1 0 0 0 0 1 1 0 1 0 1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 X 1 1 0 0 1 X
hold
reset
set
not allowed

## Slide 16: Gated R-S latch
enable'
S'
Q'
Q
R'
R
S
Control when R and S inputs matter
  otherwise, the slightest glitch on R or S while enable is low could cause change in value stored
Set
Reset
S'
R'
enable'
Q
Q'
100

## Slide 17: Clocks
period
duty cycle (in this case, 50%)
Used to keep time
  wait long enough for inputs (R' and S') to settle
  then allow to have effect on value stored
Clocks are regular periodic signals
  period (time between ticks)
  duty-cycle (time clock is high between ticks - expressed as % of period)

## Slide 18: Clocks (cont’d)
clock’
R’ and S’
changing
stable
changing
stable
stable
Controlling an R-S latch with a clock
  can't let R and S change while clock is active (allowing R and S to pass)
  only have half of clock period for signal changes to propagate
  signals must be stable for the other half of clock period
clock’
S’
Q’
Q
R’
R
S

## Slide 19: Cascading latches
clock
R
S
Q
Q’
R
S
Q
Q’
R
S
Connect output of one latch to input of another
How to stop changes from racing through chain?
  need to be able to control flow of data from one latch to the next
  move one latch per clock period
  have to worry about logic between latches (arrows) that is too fast

## Slide 20: Airlock Chamber

## Slide 21: Master-slave structure
Break flow by alternating clocks (like an air-lock)
  use positive clock to latch inputs into one R-S latch
  use negative clock to change outputs with another R-S latch
View pair as one basic unit
  master-slave flip-flop
  twice as much logic
  output changes a few gate delays after the falling edge of clock but does not affect any cascaded flip-flops
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
R
S

## Slide 22: The 1s catching problem
Set
1s catch
S
R
CLK
P
P’
Q
Q’
Reset
Master Outputs
Slave Outputs
In first R-S stage of master-slave FF
  0-1-0 glitch on R or S while clock is high is "caught" by master stage
  leads to constraints on logic to be hazard-free
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
R
S

## Slide 23: D flip-flop
10 gates
Make S and R complements of each other
  eliminates 1s catching problem
  can't just hold previous value (must have new value ready every clock period)
  value of D just before clock goes low is what is stored in flip-flop
  can make R-S flip-flop by adding logic to make D = S + R’ Q
D
Q
Q’
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’

## Slide 24: Edge-triggered flip-flops
Q
D
Clk=1
R
S
0
D’
0
D’
D
Q’
negative edge-triggered D flip-flop (D-FF)
4-5 gate delays
must respect setup and hold time constraints to successfully capture input
characteristic equation Q(t+1) = D
holds D’ when
clock goes low
holds D when clock goes low
More efficient solution: only 6 gates
  sensitive to inputs only near edge of clock signal (not while high)

## Slide 25: Edge-triggered flip-flops (cont’d)
Q
D
Clk=0
R
S
D
D’
D’
D’
D
when clock goes high-to-low
data is latched
when clock is low
data is held
Step-by-step analysis
Q
new D
Clk=0
R
S
D
D’
D’
D’
D
new D  old D

## Slide 26: Edge-triggered flip-flops (cont’d)
positive edge-triggered FF
negative edge-triggered FF
D
CLK
Qpos
Qpos’
Qneg
Qneg’
100
Positive edge-triggered
  inputs sampled on rising edge; outputs change after rising edge
Negative edge-triggered flip-flops
  inputs sampled on falling edge; outputs change after falling edge

## Slide 27: Timing methodologies
Rules for interconnecting components and clocks
  guarantee proper operation of system when strictly followed
Approach depends on building blocks used for memory elements
  we'll focus on systems with edge-triggered flip-flops
    found in programmable logic devices
  many custom integrated circuits focus on level-sensitive latches
Basic rules for correct timing:
  (1) correct inputs, with respect to time, are provided to the flip-flops
  (2) no flip-flop changes state more than once per clocking event

## Slide 28: Timing methodologies (cont’d)
there is a timing "window" around the clocking event during which the input must remain stable and unchanged in order to be recognized
clock
data
changing
stable
input
clock
Tsu
Th
clock
data
D
Q
D
Q
Definition of terms
  clock: periodic event, causes state of memory element to change can be rising edge or falling edge or high level or low level
  setup time: minimum time before the clocking event by which the input must be stable (Tsu)
  hold time: minimum time after the clocking event until which the input must remain stable (Th)

## Slide 29: Comparison of latches and flip-flops
behavior is the same unless input changes
while the clock is high
D Q
CLK
positive edge-triggered flip-flop
D Q
G
CLK
transparent (level-sensitive) latch
D
CLK
Qedge
Qlatch

## Slide 30: Comparison of latches and flip-flops (cont’d)
Type When inputs are sampled When output is valid
unclocked always propagation delay from input change latch
level-sensitive clock high propagation delay from input change latch (Tsu/Th around falling or clock edge (whichever is later) edge of clock)
master-slave clock hi-to-lo transition propagation delay from falling edge flip-flop (Tsu/Th around falling of clock edge of clock)
negative clock hi-to-lo transition propagation delay from falling edge edge-triggered (Tsu/Th around falling of clock flip-flop edge of clock)

## Slide 31: Typical timing specifications
all measurements are made from the clocking event (the rising edge of the clock)
Positive edge-triggered D flip-flop
  setup and hold times
  minimum clock width
  propagation delays (low to high, high to low, max and typical)
D
Clk
Q
T
su
1.8
ns
T
h
0.5
ns
T
w
3.3
ns
T
pd
3.6 ns
1.1 ns
T
su
1.8
ns
T
h
0.5
ns
T
pd
3.6 ns
1.1 ns
T
w
3.3
ns

## Slide 32: Cascading edge-triggered flip-flops
IN
Q0
Q1
CLK
100
Shift register
  new value goes into first stage
  while previous value of first stage goes into second stage
  consider setup/hold/propagation delays (prop must be > hold)
CLK
IN
Q0
Q1
D
Q
D
Q
OUT

## Slide 33: Cascading edge-triggered flip-flops (cont’d)
timing constraints
guarantee proper
operation of
cascaded components
assumes infinitely fast distribution of the clock
Why this works
  propagation delays exceed hold times
  clock width constraint exceeds setup time
  this guarantees following stage will latch current value before it changes to new value
Tsu
1.8ns
Tp
1.1-3.6ns
Th
0.5ns
In
Q0
Q1
CLK
Tsu
1.8ns
Tp
1.1-3.6ns
Th
0.5ns

## Slide 34: Clock skew
original state: IN = 0, Q0 = 1, Q1 = 1
due to skew, next state becomes: Q0 = 0, Q1 = 0, and not Q0 = 0, Q1 = 1
CLK1 is a delayed
version of CLK0
In
Q0
Q1
CLK0
CLK1
100
The problem
  correct behavior assumes next state of all storage elements determined by all storage elements at the same time
  this is difficult in high-performance systems because time for clock to arrive at flip-flop is comparable to delays through logic
  effect of skew on cascaded flip-flops:

## Slide 35: Summary of latches and flip-flops
Development of D-FF
  level-sensitive used in custom integrated circuits
    can be made with 4 switches
  edge-triggered used in programmable logic devices
  good choice for data storage register
Historically J-K FF was popular but now never used
  similar to R-S but with 1-1 being used to toggle output (complement state)
  good in days of TTL/SSI (more complex input function: D = J Q’ + K’ Q
  not a good choice for PALs/PLAs as it requires 2 inputs
  can always be implemented using D-FF
Preset and clear inputs are highly desirable on flip-flops
  used at start-up or to reset system to a known state

## Slide 36: Metastability and asynchronous inputs
Clocked synchronous circuits
  inputs, state, and outputs sampled or changed in relation to a common reference signal (called the clock)
  e.g., master/slave, edge-triggered
Asynchronous circuits
  inputs, state, and outputs sampled or changed independently of a common reference signal (glitches/hazards a major concern)
  e.g., R-S latch
Asynchronous inputs to synchronous circuits
  inputs can change at any time, will not meet setup/hold times
  dangerous, synchronous inputs are greatly preferred
  cannot be avoided (e.g., reset signal, memory wait, user input)

## Slide 37: Handling asynchronous inputs
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
Clocked
Synchronous
System
Synchronizer
Never allow asynchronous inputs to fan-out to more than one flip-flop
  synchronize as soon as possible and then treat as synchronous signal

## Slide 38: Handling asynchronous inputs (cont’d)
In is asynchronous and fans out to D0 and D1 one FF catches the signal, one does not
inconsistent state may be reached!
In
Q0
Q1
CLK
What can go wrong?
  input changes too close to clock edge (violating setup time constraint)

## Slide 39: Synchronization failure
small, but non-zero probability that the FF output will get stuck in an in-between state
oscilloscope traces demonstrating
synchronizer failure and eventual
decay to steady state
logic 0
logic 1
logic 0
logic 1
Occurs when FF input changes close to clock edge
  the FF may enter a metastable state – neither a logic 0 nor 1 –
  it may stay in this state an indefinite amount of time
  this is not likely in practice but has some probability

## Slide 40: Dealing with synchronization failure
asynchronous
input
synchronous system
D
D
Q
Q
synchronized
input
Clk
Probability of failure can never be reduced to 0, but it can be reduced
  (1) slow down the system clock this gives the synchronizer more time to decay into a steady state; synchronizer failure becomes a big problem for very high speed systems
  (2) use fastest possible logic technology in the synchronizer this makes for a very sharp "peak" upon which to balance
  (3) cascade two synchronizers this effectively synchronizes twice (both would have to fail)

## Slide 41: Flip-flop features
Reset (set state to 0) – R
  synchronous: Dnew = R' • Dold (when next clock edge arrives)
  asynchronous: doesn't wait for clock, quick but dangerous
Preset or set (set state to 1) – S (or sometimes P)
  synchronous: Dnew = Dold + S (when next clock edge arrives)
  asynchronous: doesn't wait for clock, quick but dangerous
Both reset and preset
  Dnew = R' • Dold + S (set-dominant)
  Dnew = R' • Dold + R'S (reset-dominant)
Selective input capability (input enable or load) – LD or EN
  multiplexor at input: Dnew = LD' • Q + LD • Dold
  load may or may not override reset/set (usually R/S have priority)
Complementary outputs – Q and Q'

## Slide 42: Registers
R
S
R
S
R
S
D
Q
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
OUT4
CLK
IN1
IN2
IN3
IN4
R
S
"0"
Collections of flip-flops with similar controls and logic
  stored values somehow related (for example, form binary value)
  share clock, reset, and set lines
  similar logic at each stage
Examples
  shift registers
  counters

## Slide 43: Shift register
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Holds samples of input
  store last 4 input values in sequence
  4-bit shift register:

## Slide 44: Universal shift register
clear sets the register contents and output to 0 s1 and s0 determine the shift function s0 s1 function 0 0 hold state 0 1 shift right 1 0 shift left 1 1 load new input
left_in
left_out
right_out
clear
right_in
output
input
s0
s1
clock
Holds 4 values
  serial or parallel inputs
  serial or parallel outputs
  permits shift left or right
  shift in new values from left or right

## Slide 45: Design of universal shift register
Nth cell
D
Q
CLK
Q[N-1] (left)
Q[N+1] (right)
Input[N]
to N-1th cell
to N+1th cell
clear s0 s1 new value 1 – – 0 0 0 0 output 0 0 1 output value of FF to left (shift right) 0 1 0 output value of FF to right (shift left) 0 1 1 input
Consider one of the four flip-flops
  new value at next clock cycle:
s0 and s1 control mux
0
1
2
3
CLEAR

## Slide 46: Shift register application
parallel inputs
parallel outputs
serial transmission
Parallel-to-serial conversion for serial transmission

## Slide 47: Pattern recognizer
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
OUT
Combinational function of input samples
  in this case, recognizing the pattern 1001 on the single input signal

## Slide 48: Counters
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Sequences through a fixed set of patterns
  in this case, 1000, 0100, 0010, 0001
  if one of the patterns is its initial state (by loading or set/reset)

## Slide 49: Activity
How does this counter work?
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Counts through the sequence: 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
Known as Mobius (or Johnson) counter

## Slide 50: Binary counter
D
Q
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
OUT4
CLK
"1"
Logic between registers (not just multiplexer)
  XOR decides when bit should be toggled
  always for low-order bit, only when first bit is true for second bit, and so on

## Slide 51: Asynchronous vs. Synchronous Counters
Ripple Counters
Deceptively attractive alternative to synchronous design style
Count signal ripples from left to right
Can lead to "spiked outputs" from combinational logic
decoding the counter's state

## Slide 52: Four-bit binary synchronous up-counter
EN D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
(1) Low order 4-bits = 1111
(2) RCO goes high
(3) High order 4-bits are incremented
Standard component with many applications
  positive edge-triggered FFs w/ synchronous load and clear inputs
  parallel load data from D, C, B, A
  enable inputs: must be asserted to enable counting
  RCO: ripple-carry out used for cascading counters
    high when counter is in its highest state 1111
    implemented using an AND gate

## Slide 53: Offset counters
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "0" "0" "0"
"0"
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "1" "1" "0"
Starting offset counters – use of synchronous load
  e.g., 0110, 0111, 1000, 1001, 1010, 1011, 1100, 1101, 1111, 0110, . . .
Ending offset counter – comparator for ending value
  e.g., 0000, 0001, 0010, ..., 1100, 1101, 0000
Combinations of the above (start and stop value)

## Slide 54: Hardware Description Languages and Sequential Logic
Flip-flops
  representation of clocks - timing of state changes
  asynchronous vs. synchronous
Shift registers
Simple counters

## Slide 55: Flip-flop in Verilog
module dff (clk, d, q);
input clk, d; output q; reg q;
always @(posedge clk) q = d;
endmodule
Use always block's sensitivity list to wait for clock edge

## Slide 56: More Flip-flops
module dff (clk, s, r, d, q); input clk, s, r, d; output q; reg q;
always @(posedge clk) if (r) q = 1'b0; else if (s) q = 1'b1; else q = d;
endmodule
module dff (clk, s, r, d, q); input clk, s, r, d; output q; reg q;
always @(posedge r) q = 1'b0; always @(posedge s) q = 1'b1; always @(posedge clk) q = d;
endmodule
Synchronous/asynchronous reset/set
  single thread that waits for the clock
  three parallel threads – only one of which waits for the clock
Synchronous
Asynchronous

## Slide 57: Incorrect Flip-flop in Verilog
module dff (clk, d, q);
input clk, d; output q; reg q;
always @(clk) q = d;
endmodule
Use always block's sensitivity list to wait for clock to change
Not correct! Q will
change whenever the
clock changes, not
just on an edge.

## Slide 58: Blocking and Non-Blocking Assignments
always @(posedge CLK) begin temp = B; B = A; A = temp; end
always @(posedge CLK) begin A <= B; B <= A; end
Blocking assignments (X=A)
  completes the assignment before continuing on to next statement
Non-blocking assignments (X<=A)
  completes in zero time and doesn’t change the value of the target until a blocking point (delay/wait) is encountered
Example: swap

## Slide 59: Register-transfer-level (RTL) Assignment
Non-blocking assignment is also known as an RTL assignment
  if used in an always block triggered by a clock edge
  all flip-flops change together
// B,C,D all get the value of A always @(posedge clk) begin B = A; C = B; D = C; end
// implements a shift register too always @(posedge clk) begin B <= A; C <= B; D <= C; end

## Slide 60: Mobius Counter in Verilog
initial begin A = 1’b0; B = 1’b0; C = 1’b0; D = 1’b0; end always @(posedge clk) begin A <= ~D; B <= A; C <= B; D <= C; end

## Slide 61: Binary Counter in Verilog
module binary_counter (clk, c8, c4, c2, c1);
input clk; output c8, c4, c2, c1;
reg [3:0] count;
initial begin count = 0; end always @(posedge clk) begin count = count + 4’b0001; end
assign c8 = count[3]; assign c4 = count[2]; assign c2 = count[1]; assign c1 = count[0]; endmodule
module binary_counter (clk, c8, c4, c2, c1, rco);
input clk; output c8, c4, c2, c1, rco;
reg [3:0] count; reg rco;
initial begin . . . end always @(posedge clk) begin . . . end
assign c8 = count[3]; assign c4 = count[2]; assign c2 = count[1]; assign c1 = count[0]; assign rco = (count == 4b’1111); endmodule

## Slide 62: Sequential logic summary
Fundamental building block of circuits with state
  latch and flip-flop
  R-S latch, R-S master/slave, D master/slave, edge-triggered D flip-flop
Timing methodologies
  use of clocks
  cascaded FFs work because propagation delays exceed hold times
  beware of clock skew
Asynchronous inputs and their dangers
  synchronizer failure: what it is and how to minimize its impact
Basic registers
  shift registers
  counters
Hardware description languages and sequential logic