## Slide 1: Chapter 8: Working with Finite State Machines

## Slide 2: Motivation
Basic FSM Design Procedure:
(1) Understand the problem
(2) Obtain a formal description
(3) Minimize number of states
(4) Encode the states
(5) Choose FFs to implement state register
(6) Implement the FSM

## Slide 3: Motivation
State Reduction
Odd Parity Checker: two alternative state diagrams
Identical output behavior on all input strings
FSMs are equivalent, but require different implementations
Design state diagram without concern for # of states,
Reduce later

## Slide 4: Finite state machine optimization
State minimization
  fewer states require fewer state bits
  fewer bits require fewer logic equations
Encodings: state, inputs, outputs
  state encoding with fewer bits has fewer equations to implement
    however, each may be more complex
  state encoding with more bits (e.g., one-hot) has simpler equations
    complexity directly related to complexity of state diagram
  input/output encoding may or may not be under designer control

## Slide 5: Algorithmic approach to state minimization
Goal – identify and combine states that have equivalent behavior
Equivalent states:
  same output
  for all input combinations, states transition to same or equivalent states

## Slide 6: Algorithmic approach to state minimization
Two approaches:
  Category 1:
    1. Assume that all states ARE NOT EQUIVALENT.
     Place all states in different sets.
    2. Find two equivalent states and merge them into one state.
    3. Repeat (2) until no equivalent states are found.
  Category 2:
    1. Assume that all states ARE EQUIVALENT.
     Place all states in one set
    2. initially partition set based on output behavior
    3. successively partition resulting subsets based on next state transitions
    4. repeat (3) until no further partitioning is required
  States left in the same set are equivalent

## Slide 7: Category 1 vs. Category 2
Q: Are they equivalent?
Q: Is Category 1 better than Category 2?
Q: Is Category 2 better than Category 1?

## Slide 8: State Reduction
Category 1: Row Matching Method
Example FSM Specification:
Single input X, output Z
Taking inputs grouped four at a time, output 1 if last four inputs
were the string 1010 or 0110
Example I/O Behavior:
X = 0010 0110 1100 1010 0011 . . .
Z = 0000 0001 0000 0001 0000 . . .
Upper bound on FSM complexity:
Fifteen states (1 + 2 + 4 + 8)
Thirty transitions (2 + 4 + 8 + 16)
sufficient to recognize any binary string of length four!

## Slide 9: State Reduction
Row Matching Method
State Diagram for Example FSM:

## Slide 10: State Reduction
Row Matching Method
Initial State Transition Table:

## Slide 11: State Reduction
Row Matching Method
Initial State Transition Table:

## Slide 12: State Reduction
Row Matching Method

## Slide 13: State Reduction
Row Matching Method

## Slide 14: State Reduction
Row Matching Method

## Slide 15: State Reduction
Row Matching Method

## Slide 16: State Reduction
Row Matching Method
Final Reduced
State Transition Table
Corresponding State
Diagram

## Slide 17: State minimization example
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
Sequence detector for 010 or 110
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0

## Slide 18: Category 2: Method of successive partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6

## Slide 19: Minimized FSM
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
State minimized sequence detector for 010 or 110
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0

## Slide 20: Category 1 vs. Category 2
Q: Are they equivalent?
Q: Is Category 1 better than Category 2?
Q: Is Category 2 better than Category 1?

## Slide 21: State Reduction
Row Matching Method
Straightforward to understand and easy to implement
Problem: does not yield the most reduced state table!
Example: 3 State Odd Parity Checker
No way to combine states S0 and S2
based on Next State Criterion!

## Slide 22: More complex state minimization
symbolic state transition table
present next state output state 00 01 10 11 S0 S0 S1 S2 S3 1 S1 S0 S3 S1 S4 0 S2 S1 S3 S2 S4 1 S3 S1 S0 S4 S5 0 S4 S0 S1 S2 S5 1 S5 S1 S4 S0 S5 0
inputs here
Multiple input example
10
01
11
00
00
01
11
10
10
01
11
00
10
00
11
00
11
10
01
10
11
01
00
S0 [1]
S2 [1]
S4 [1]
S1
[0]
S3
[0]
S5
[0]
01

## Slide 23: State Reduction
Category 2: Implication Chart Method
New example FSM:
Single input X, Single output Z
Output a 1 whenever the serial sequence 010 or 110 has been
observed at the inputs
State transition table:

## Slide 24: State Reduction
Implication Chart Method
Enumerate all possible combinations of states taken two at a time
Naive Data Structure:
Xij will be the same as Xji
Also, can eliminate the diagonal
Implication Chart
Next States
Under all
Input
Combinations

## Slide 25: State Reduction
Implication Chart
Filling in the Implication Chart
Entry Xij: Row is Si, Column is Sj
Si is equivalent to Sj if outputs are the same and
next states are equivalent
Xij contains the next states of Si, Sj which must be equivalent if
Si and Sj are equivalent
If Si, Sj have different output behavior, then Xij is crossed out
Example:
S0 transitions to S1 on 0, S2 on 1;
S1 transitions to S3 on 0, S4 on 1;
So square X<0,1> contains entries S1-S3 (transition on zero)
S2-S4 (transition on one)
S1-S3
S2-S4
S0
S1

## Slide 26: State Reduction
Implication Chart Method
Starting Implication Chart
S2 and S4
have different
I/O behavior
This implies that
S1 and S0 cannot
be combined

## Slide 27: State Reduction
Implication Chart Method
Results of First Marking Pass
Second Pass Adds No New Information
S3 and S5 are equivalent
S4 and S6 are equivalent
This implies that S1 and S2 are too!
Reduced State
Transition Table

## Slide 28: State Reduction
Multiple Input State Diagram Example
State Diagram
Symbolic State Diagram

## Slide 29: State Reduction
Multiple Input Example
Implication Chart
Minimized State Table

## Slide 30: Minimized FSM
S0-S1
S1-S3
S2-S2
S3-S4
S0-S0
S1-S1
S2-S2
S3-S5
S0-S1
S3-S0
S1-S4
S4-S5
S0-S1
S3-S4
S1-S0
S4-S5
S1-S0
S3-S1
S2-S2
S4-S5
S4-S0
S5-S5
S1-S1
S0-S4
minimized state table
(S0==S4) (S3==S5)
present next state output state 00 01 10 11 S0' S0' S1 S2 S3' 1 S1 S0' S3' S1 S3' 0 S2 S1 S3' S2 S0' 1 S3' S1 S0' S0' S3' 0
Implication chart method
  cross out incompatible states based on outputs
  then cross out more cells if indexed chart entries are already crossed out
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4

## Slide 31: State Reduction
Implication Chart Method
Does the method solve the problem with the odd parity checker?
Implication Chart
S0 is equivalent to S2
since nothing contradicts this assertion!

## Slide 32: State Reduction
Implication Chart Method
The detailed algorithm:
1. Construct implication chart, one square for each combination of states taken two at a time
2. Square labeled Si, Sj, if outputs differ than square gets "X". Otherwise write down implied state pairs for all input combinations
3. Advance through chart top-to-bottom and left-to-right. If square Si, Sj contains next state pair Sm, Sn and that pair labels a square already labeled "X", then Si, Sj is labeled "X".
4. Continue executing Step 3 until no new squares are marked with "X".
5. For each remaining unmarked square Si, Sj, then Si and Sj are equivalent.

## Slide 33: Minimizing incompletely specified FSMs
Equivalence of states is transitive when machine is fully specified
But its not transitive when don't cares are present e.g., state output S0 – 0 S1 is compatible with both S0 and S2 S1 1 – but S0 and S2 are incompatible S2 – 1
No polynomial time algorithm exists for determining best grouping of states into equivalent sets that will yield the smallest number of final states

## Slide 34: Minimizing states may not yield best circuit
X Q1 Q0 Q1+ Q0+ 0 0 0 0 0 0 0 1 0 0 0 1 1 0 0 1 0 0 0 1 1 0 1 1 1 1 1 1 1 1 – 1 0 0 0
Q1+ = X (Q1 xor Q0)
Q0+ = X Q1’ Q0’
Example: edge detector - outputs 1 when last two input changes from 0 to 1
00 [0]
11
[0]
01 [1]
X’
X’
X’
X
X
X

## Slide 35: Another implementation of edge detector
"Ad hoc" solution - not minimal but cheap and fast
00 [0]
10
[0]
01 [1]
X’
X
X’
X
X
X
11 [0]
X’
X’

## Slide 36: State assignment
Choose bit vectors to assign to each “symbolic” state
  with n state bits for m states there are 2n! / (2n – m)! [m <= 2n]
  2n codes possible for 1st state, 2n–1 for 2nd, 2n–2 for 3rd, …
  huge number even for small values of n and m
    intractable for state machines of any size
    heuristics are necessary for practical solutions
  optimize some metric for the combinational logic
    size (amount of logic and number of FFs)
    speed (depth of logic and fanout)
    dependencies (decomposition)

## Slide 37: State Assignment
When FSM implemented with gate logic, number of gates will depend on
mapping between symbolic state names and binary encodings
4 states = 4 choices for first state, 3 for second, 2 for third, 1 for last
= 24 different encodings (4!)
Example for State Assignment: Traffic Light Controller
Symbolic State Names: HG, HY, FG, FY
24 state assignments
for the traffic light
controller

## Slide 38: State assignment strategies
Possible strategies
  sequential – just number states as they appear in the state table
  random – pick random codes
  one-hot – use as many state bits as there are states (bit=1 –> state)
  output – use outputs to help encode states
  heuristic – rules of thumb that seem to work in most cases
No guarantee of optimality – another intractable problem

## Slide 39: State Assignment
Pencil & Paper Heuristic Methods
State Maps: similar in concept to K-maps
If state X transitions to state Y, then assign "close" assignments
to X and Y
S
0
S
1
S
2
S
3
S
4
0
1

## Slide 40: State Assignment
Paper and Pencil Methods
Minimum Bit Distance Criterion
13
7
Traffic light controller: HG = 00, HY = 01, FG = 11, FY = 10
yields minimum distance encoding but not best assignment!
Transition
S0 to S1:
S0 to S2:
S1 to S3:
S2 to S3:
S3 to S4:
S4 to S1:
First Assignment
Bit Changes
2
3
3
2
1
2
Second Assignment
Bit Changes
1
1
1
1
1
2

## Slide 41: Why State Assignment?
Effect of Two State Encodings
First encoding exhibits a better clustering of 1's in the next state map

## Slide 42: State Assignment
Paper & Pencil Methods
Alternative heuristics based on input and output behavior as well
as transitions:
Adjacent assignments to:
states that share a common next state
(group 1's in next state map)
states that share a common ancestor state
(group 1's in next state map)
states that have common output behavior
(group 1's in output map)

## Slide 43: Heuristics for state assignment
I Q Q+ O i a c j i b c k
I Q Q+ O i a b j k a c l
I Q Q+ O i a b j i c d j
c = i * a + i * b
b = i * a c = k * a
j = i * a + i * c b = i * a d = i * c
i / j
i / k
a
b
c
a
b
c
i / j
k / l
b
d
i / j
a
c
i / j
Adjacent codes to states that share a common next state
  group 1's in next state map
Adjacent codes to states that share a common ancestor state
  group 1's in next state map
Adjacent codes to states that have a common output behavior
  group 1's in output map

## Slide 44: State Assignment
Pencil and Paper Methods
Example: 3-bit Sequence Detector
Highest Priority: (S3', S4')
Medium Priority: (S3', S4')
Lowest Priority:
0/0: (S0, S1', S3')
1/0: (S0, S1', S3', S4')

## Slide 45: State Assignment
Paper and Pencil Methods
Reset State = 00
Highest Priority Adjacency
Not much difference in these two
assignments

## Slide 46: State Assignment
Paper & Pencil Methods
Highest Priority: (S3', S4'), (S7', S10')
Medium Priority:
(S1, S2), 2x(S3', S4'), (S7', S10')
Lowest Priority:
0/0: (S0, S1, S2, S3', S4', S7')
1/0: (S0, S1, S2, S3', S4', S7')
Another Example: 4 bit String Recognizer

## Slide 47: State Assignment
Paper & Pencil Methods
00 = Reset = S0
(S1, S2), (S3', S4'), (S7', S10')
placed adjacently

## Slide 48: State Assignment
Effect of Adjacencies on Next State Map
First encoding exhibits a better clustering of 1's in the next state map

## Slide 49: State Assignment
One Hot Encodings
n states encoded in n flipflops
HG = 0001
HY = 0010
FG = 0100
FY = 1000
.i 7
.o 9
.ilb c tl ts q3 q2 q1 q0
.ob p3 p2 p1 p0 st h1 h0 f1 f0
.p 10
0-- 0001 0001 00010
-0- 0001 0001 00010
11- 0001 0010 10010
--0 0010 0010 00110
--1 0010 0100 10110
10- 0100 0100 01000
0-- 0100 1000 11000
-1- 0100 1000 11000
--0 0010 1000 01001
--1 0010 0001 11001
.e
Espresso Inputs
.i 7
.o 9
.ilb c tl ts q3 q2 q1 q0
.ob p3 p2 p1 p0 st h1 h0 f1 f0
.p 8
10-0100 010001000
11-0001 001010010
-0-0001 000100010
0--0001 000100010
0--0100 100011000
-1-0100 100011000
--00010 101001111
--10010 010111111
.e
Espresso Outputs
Notes: Next state logic and outputs get simpler because each state is represented by one bit without endcoding.

## Slide 50: One-hot state assignment
Simple
  easy to encode
  easy to debug
Small logic functions
  each state function requires only predecessor state bits as input
Good for programmable devices
  lots of flip-flops readily available
  simple functions with small support (signals its dependent upon)
Impractical for large machines
  too many states require too many flip-flops
  decompose FSMs into smaller pieces that can be one-hot encoded
Many slight variations to one-hot
  one-hot + encoded

## Slide 51: Output-based encoding
Reuse outputs as state bits - use outputs to help distinguish states
  why create new functions for state bits when output can serve as well
  fits in nicely with synchronous Mealy implementations
HG = ST’ H1’ H0’ F1 F0’ + ST H1 H0’ F1’ F0 HY = ST H1’ H0’ F1 F0’ + ST’ H1’ H0 F1 F0’ FG = ST H1’ H0 F1 F0’ + ST’ H1 H0’ F1’ F0’ FY = ST H1 H0’ F1’ F0’ + ST’ H1 H0’ F1’ F0
Output patterns are unique to states, we do not need ANY state bits – implement 5 functions (one for each output) instead of 7 (outputs plus 2 state bits)
Inputs Present State Next State Outputs C TL TS ST H F 0 – – HG HG 0 00 10 – 0 – HG HG 0 00 10 1 1 – HG HY 1 00 10 – – 0 HY HY 0 01 10 – – 1 HY FG 1 01 10 1 0 – FG FG 0 10 00 0 – – FG FY 1 10 00 – 1 – FG FY 1 10 00 – – 0 FY FY 0 10 01 – – 1 FY HG 1 10 01

## Slide 52: Finite State Machine Partitioning
Why Partition?
mapping FSMs onto programmable logic components:
limited number of input/output pins
limited number of product terms or other programmable resources
Example of Input/Output Partitioning:
5 outputs depend on 15 inputs
5 outputs depend on different overlapping set of 15 inputs

## Slide 53: Finite State Machine Partitioning
Introduction of Idle States
Before Partitioning

## Slide 54: Finite State Machine Partitioning
After Partitioning
Introduction of Idle States
S1
S2
S3
C4
C1
C3+C5
SA
C2•S6
C2•S6
S6
S5
S4
C5•S2
C2
SB
C1•S1
C3•S2 +
C4•S3
C1•S1 + C3•S2 + C4•S3 + C5•S2

## Slide 55: Finite State Machine Partitioning
Rules for Partitioning
Rule #1: Source State Transformation; SA is the Idle State
Rule #2: Destination State Transformation
S1
S6
C2
SA
S1
C2•S6

## Slide 56: Finite State Machine Partitioning
Rules for Partitioning
Rule #3: Multiple Transitions with Same Source or Destination
Rule #4: Hold Condition for Idle State
S2
S3
S5
S4
C4
C5
C3
S2
S3
SA
C3+C5
C4
S5
S4
C5•S2
SB
C3•S2 +
C4•S3
SA
S1
C2•S6
C2•S6

## Slide 57: Finite State Machine Partitioning
Another Example
6 state up/down counter
building block has 2 FFs + combinational logic

## Slide 58: Finite State Machine Partitioning
6 State Up/Down Counter
S0
S1
S2
D
D
U
U
SA
D
U
D • S3
U • S5
U • S5 + D • S3
S5
S4
S3
D
D
U
U
SB
U
D
D • S0
U • S2
D • S0 + U • S2
Introduction of the two idle state SA, SB
Count sequence S0, S1, S2, S3, S4, S5:
S2 goes to SA and holds, leaves after S5
S5 goes to SB and holds, leaves after S2
Down sequence is similar

## Slide 59: Sequential logic optimization summary
State minimization
  straightforward in fully-specified machines
  computationally intractable, in general (with don’t cares)
State assignment
  many heuristics
  best-of-10-random just as good or better for most machines
  output encoding can be attractive (especially for PAL implementations)