## Slide 1: Chapter 9: Sequential Logic Technologies

## Slide 2: Sequential logic implementation
Basic Sequential Logic Components
FSM Design with Counters
FSM Design with Programmable Logic Devices
Case Study: Traffic-Light Controller

## Slide 3: (+) of Set/Reset Inputs: Median filter FSM
Remove single 0s between two 1s (output = PS3)
000
0
1
0
100
010
110
111
011
001
1
1
1
1
1
1
0
0
0
0
0
Reset
I PS1 PS2 PS3 NS1 NS2 NS3 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 0 0 0 1 0 0 1 0 1 X X X 0 1 1 0 0 1 1 0 1 1 1 0 1 1 1 0 0 0 1 0 0 1 0 0 1 1 0 0 1 0 1 0 1 1 1 1 0 1 1 1 1 1 1 1 0 0 1 1 0 1 1 0 1 X X X 1 1 1 0 1 1 1 1 1 1 1 1 1 1

## Slide 4: Median filter FSM (cont’d)
Realized using the standard procedure and individual FFs and gates
I PS1 PS2 PS3 NS1 NS2 NS3 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 0 0 0 1 0 0 1 0 1 X X X 0 1 1 0 0 1 1 0 1 1 1 0 1 1 1 0 0 0 1 0 0 1 0 0 1 1 0 0 1 0 1 0 1 1 1 1 0 1 1 1 1 1 1 1 0 0 1 1 0 1 1 0 1 X X X 1 1 1 0 1 1 1 1 1 1 1 1 1 1
NS1 = Reset’ (I)
NS2 = Reset’ ( PS1 + PS2 I )
NS3 = Reset’ PS2
O = PS3

## Slide 5: Median filter FSM (cont’d)
But it looks like a shift register if you look at it right
000
0
1
0
100
010
110
111
011
001
1
1
1
1
1
1
0
0
0
0
0
Reset
000
0
1
0
100
010
110
111
011
001
1
1
1
1
1
1
0
0
0
0
0
Reset
101
1
0

## Slide 6: Median filter FSM (cont’d)
An alternate implementation with S/R FFs
The set input (S) does the median filter function by making the next state 111 whenever the input is 1 and PS2 is 1 (1 input to state x1x)
R = Reset
S = PS2 I
NS1 = I
NS2 = PS1
NS3 = PS2
O = PS3
Out
CLK
D
Q
R
S
D
Q
R
S
D
Q
R
S
In
Reset

## Slide 7
FSM Design with Counters
Synchronous Counters: CLR, LD, CNT
Four kinds of transitions for each state:
(1) to State 0 (CLR)
(2) to next state in sequence (CNT)
(3) to arbitrary next state (LD)
(4) loop in current state
Careful state assignment is needed to reflect basic sequencing
of the counter

## Slide 8
ROM-based Design
Example: BCD to Excess 3 Serial Converter
BCD Excess 3 Code
0000 0011
0001 0100
0010 0101
0011 0110
0100 0111
0101 1000
0110 1001
0111 1010
1000 1011
1001 1100
Conversion Process
Bits are presented in bit serial fashion
starting with the least significant bit
Single input X, single output Z

## Slide 9: Implementation Strategies
BCD to Excess-3 Converter
State Transition Table
Derived State Diagram

## Slide 10
FSM Design with Counters
Excess 3 Converter Revisited
Note the sequential nature
of the state assignments

## Slide 11
FSM Design with Counters
Excess 3 Converter
CLR signal dominates LD which dominates Count
Inputs/Current
State
Next
State
Outputs
X
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
Q2
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
Q1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
Q0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
Q2+
0
0
0
0
1
0
0
X
1
1
0
0
1
1
X
X
Q1+
0
1
1
0
0
1
0
X
0
0
1
0
0
1
X
X
Q0+
1
0
1
0
1
1
0
X
0
1
1
0
1
0
X
X
Z
1
1
0
0
0
1
1
X
0
0
1
1
1
0
X
X
CLR
1
1
1
0
1
1
0
X
1
1
1
0
1
1
X
X
LD
1
1
1
X
1
0
X
X
0
0
1
X
1
1
X
X
EN
1
1
1
X
1
X
X
X
X
X
1
X
1
1
X
X
C
X
X
X
X
X
0
X
X
1
1
X
X
X
X
X
X
B
X
X
X
X
X
1
X
X
0
0
X
X
X
X
X
X
A
X
X
X
X
X
1
X
X
0
1
X
X
X
X
X
X

## Slide 12
FSM Implementation with Counters
Excess 3 Converter Schematic
Synchronous Output Register

## Slide 13
FSM Design with Programmable Logic
Block Diagram for
Synchronous Mealy Machine
ROM-based Realization
Inputs & Current State
form the address
ROM data bits form the
Outputs & Next State

## Slide 14: Implementation Strategies
BCD to Excess 3 Converter
ROM-based Implementation
Truth Table/ROM I/Os
Circuit Level Realization
74175 = 4 x positive edge triggered D FFs
In ROM-based designs, no need to consider state assignment

## Slide 15
BCD to Excess-3 Converter
Timing Behavior for input strings 0 0 0 0 (0) and 1 1 1 0 (7)
0 0 0 0 1 1 0 0
1 1 1 0 0 1 0 1
LSB
MSB
LSB
LSB